## Slide 1: HIRES Technical concept and design

## Slide 2: HIRES requirements/goals
HR
Full l-coverage (0.35-2.5mm) in a single exposure
RV-optimized, ultra-stable HR mode R~100,000
Throughput-optimized HR mode R~100,000
Polarimetric capabilities
Others
Throughput-optimized MR mode R~10,000
Some multi-objects capabilities in MR
Diffraction limited IFU/slit with R~100,000 at IR l’s

## Slide 3: HIRES basic physics of ELTs
Adaptive optics do not help much below 1.2 mm, and are virtually useless below 1 mm
 HIRES must be designed for seeing limited PSF
Cannot make a instrument with a grating of ~10m
 HIRES cannot be a genuine, HR-optimized spectrometer
  HIRES is intrinsically a MR-optimized spectrograph
  To obtain HR one needs a long-slit and a slicer

## Slide 4: HIRES main HR-RV observing mode
Mode | R | D-fib | N.obj | Size of Res. Element |  | Comment
 |  |  |  | on-sky | pixels | 
HR-RV | 100,000 | 0.76” | 2 + lcal | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for RV (scramble etc.)
HR-HT | 100,000 | 0.76” | 2 (+lcal) | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for throughput
MR MOS | 14,500 | 0.86” | 10 | 0.86” x 0.86” | 20 x 11 | MOS on ELT 10’ fov
HR2 IFU | 80,000 | 7mas | 35 | 7mas x 7mas | 3.5 x 2 | SCAO fov 35x49 mas

## Slide 5: HIRES main HR-RV observing mode
Illumination of input slit

## Slide 6: HIRES main HR-RV observing mode
3D layout and rays tracing of HIRES-YHJ spectrometer

## Slide 7: HIRES main HR-RV observing mode
3D layout and rays trace animation of HIRES-YHJ spectrometer

## Slide 8: HIRES main HR-RV observing mode
Parameter | HIRES | CODEX | Espresso
# Fibers | 2 | 2 | 2
D-fiber | 0.76” | 0.82” | 1”
Simultaneous lcal | Always | Use sky fiber | Use sky fiber
Spectra of fibers 1,2 | On same detector | On different CCDs | On same detector
Echelle length | 1.2m | 1.6m | 1.2m
F/n of cameras(1) | F/1.0 | F/1.4 | F/1.8
# of reflections(2) | 7 | 11 | 6
# of refr. elements (2) | 9 | 8 | 7
Comparison with other HR spectrographs
In the cross-dispersion direction
Refers to the optical elements of the spectrometer

## Slide 9: HIRES other observing modes
Mode | R | D-fib | N.obj | Size of Res. Element |  | Comment
 |  |  |  | sky | pixels | 
HR-RV | 100,000 | 0.76” | 2 + lcal | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for RV (scramble etc.)
HR-HT | 100,000 | 0.76” | 2 (+lcal) | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for throughput
MR MOS | 14,500 | 0.86” | 10 | 0.86” x 0.86” | 20 x 11 | MOS on ELT 10’ fov
HR2 IFU | 80,000 | 7mas | 35 | 7mas x 7mas | 3.5 x 2 | SCAO fov 35x49 mas

## Slide 10: HIRES other observing mode
Illumination of input slit

## Slide 11: HIRES modes-switch does not affect main mode

## Slide 12: HIRES observing modes

## Slide 13: HIRES modular instrument scheme
We just described this part

## Slide 14
4 independent spectrographs fed by 4 groups of fibers
Each spectrograph/fiber sees a different l-range
Each fiber is fed through dichroics with separate ADC’s to correct atmospheric dispersion
Interface to K-fiber is cooled and includes a cold-stop, while does not have an ADC
In the medium-resolution mode there are 10 groups of fibers (i.e. 10 fiber interfaces) each looking at a different object, i.e. it is a MOS mode
HIRES modular instrument scheme

## Slide 15: HIRES: fibers interface and positioner
This part

## Slide 16: HIRES: fibers interface and positioner
4 fibers looking at the same object

## Slide 17: HIRES: fibers interface and positioner
4 spectrographs fed by 4 group of fibers
Each spectrograph/fiber sees a different l-range
Each fiber is fed through dichroics with separate ADC’s to correct atmospheric dispersion
Interface to K-fiber is cooled and includes a cold-stop, while does not need an ADC
In the medium-resolution mode there are 10 groups of fibers (i.e. 10 fiber interfaces) each looking at a different object, i.e. it is a MOS mode

## Slide 18: HIRES: fibers interface and positioner
Optical layout and rays-tracing for different zenith angles
U-K atmospheric dispersion =2” @45o  ADC fundamental
2” corresponds to 6mm (!!) on E-ELT focal plane

## Slide 19: ELT = Extremely Large effect of aTmospheric dispersion..
…ELT-MOS instruments do not foresee ADC’s !!

## Slide 20: HIRES: fibers interface and positioner
3D layout with rays-tracing at z=0o
Dfiber(HR) = 0.50mm
Dfiber(MR)= 0.57mm

## Slide 21: HIRES: fibers interface and positioner
4 spectrographs fed by 4 group of fibers
Each spectrograph/fiber sees a different l-range
Each fiber is fed through dichroics with separate ADC’s to correct atmospheric dispersion
Interface to K-fiber is cooled and includes a cold-stop, while does not have an ADC
In the medium-resolution mode there are 10 groups of fibers (i.e. 10 fiber interfaces) each looking at a different object, i.e. it is a MOS mode

## Slide 22: HIRES: fibers interface and positioner
Fiber interface is an A4-size rectangle ~10cm thick
10+ interfaces can be positioned on the Nas-focus

## Slide 23: HIRES as a MR spectrometer
Mode | R | D-fib | N.obj | Size of Res. Element |  | Comment
 |  |  |  | sky | pixels | 
HR-RV | 100,000 | 0.76” | 2 + lcal | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for RV (scramble etc.)
HR-HT | 100,000 | 0.76” | 2 (+lcal) | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for throughput
MR MOS | 14,500 | 0.86” | 10 | 0.86” x 0.86” | 20 x 11 | MOS on ELT 10’ fov
HR2 IFU | 80,000 | 7mas | 35 | 7mas x 7mas | 3.5 x 2 | SCAO fov 35x49 mas

## Slide 24
HIRES spectral sampling
MR spectral element on 220 pixels !
Is this really optimized?
… again basic physics of ELTs ...

## Slide 25: HIRES vs. OPTIMOS

## Slide 26: HIRES as an IFU spectrometer
Mode | R | D-fib | N.obj | Size of Res. Element |  | Comment
 |  |  |  | sky | pixels | 
HR-RV | 100,000 | 0.76” | 2 + lcal | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for RV (scramble etc.)
HR-HT | 100,000 | 0.76” | 2 (+lcal) | 0.127” x 5.0” | 2.8 x 63 | 1x6 slicing, optimized for throughput
MR MOS | 14,500 | 0.86” | 10 | 0.86” x 0.86” | 20 x 11 | MOS on ELT 10’ fov
HR2 IFU | 80,000 | 7mas | 35 | 7mas x 7mas | 3.5 x 2 | SCAO fov 35x49 mas
A zoom on the central pixel of present IFU’s
at the highest spectral and spatial resolutions

## Slide 27: HIRES: IFU interface
Dfiber(IFU) = 0.11mm
Dbundle(IFU) = 0.77mm

## Slide 28: HIRES: IFU, scale change and diffraction limit
Change of scale is obtained by feeding fibers with a slower beam
Nothing is changed in the spectrometer
Spectrometer is oversized, it works with a shrunk pupil image
Effective size of pupil image depends on fibers FRD
  pupil diameter is much larger than in geometric optics
  spectrometer does not work in diffraction-limit mode
 Fibers focal ratio degradation helps to get better image quality (!)

## Slide 29: HIRES: fibers transmission and positioning of modules
This part

## Slide 30
Anywhere
Nas-platform
Nas-platform
Far from
platform
HIRES: fibers transmission and positioning of modules

## Slide 31: HIRES cross-dispersed spectral format Same format for all observing modes
H 1.45-1.81 mm
orders 74-93
J 1.16-1.38 mm
orders 99-119
Y 0.97-1.14 mm
orders 118-140

## Slide 32: HIRES cross-dispersed spectral format Slit too long for full spectral coverage with 1 channel

## Slide 33: HIRES comparison R4-R6
Illumination of input slit

## Slide 34: HIRES comparison R6 – R4
R6: no anamorphics magnification before echelle

## Slide 35: HIRES with R4 echelle (H-band)
R64 1.5 x anamorphic magnification before echelle
200mm collimated beam

## Slide 36: HIRES with R4 echelle (J-band)
R64 1.5 x anamorphic magnification before echelle
200mm collimated beam

## Slide 37: HIRES with R4 echelle (Y-band)
R64 1.5 x anamorphic magnification before echelle
200mm collimated beam